## Slide 1: The NISAR Mission and Applications to Snow Hydrology
Rick Forster1, Jewell Lund1, Eli Deeb2, HP Marshall3
NISAR slides provided by Paul A Rosen, NISAR Project Scientist
Jet Propulsion Laboratory,
SnowEx Workshop: September 11, 2020
1
2
3

## Slide 2
NASA Science Focus: Capturing the Earth in Motion
NISAR will image Earth’s dynamic surface over time, providing information
on changes in ice sheets and glaciers, the evolution of natural and
managed ecosystems, earthquake and volcano deformation,
subsidence from groundwater and oil pumping, and the human impact of
these and many other phenomena.
NISAR (NASA-ISRO SAR)
ISRO (Indian Space Research Organization

## Slide 3: NISAR Science Overview and Program Context
Dynamics of Ice: Ice sheets, Glaciers, and Sea Level
  Will there be catastrophic collapse of the major ice sheets, including Greenland and West Antarctic and, if so, how rapidly will this occur?
  What will be the resulting time patterns of sea-level rise?
  How are alpine glaciers changing in relation to climate?
Ecosystems and Biomass Change
  How do changing climate and land use in forests, wetlands, and agricultural regions affect the carbon cycle and species habitats?
  What are the effects of disturbance on ecosystem functions and services?
Solid Earth Deformation: Hazard Response
  Which major fault systems are nearing release of stress via strong earthquakes?
  Can we predict future eruptions of volcanoes?
  What are optimal remote sensing strategies to mitigate disasters and monitor/manage water and hydrocarbon extraction and use
NRC 2007 Decadal Survey recommended a DESDynI Mission for near-term launch to address important scientific questions of high societal impact.
NASA’s Climate Architecture identified the radar’s important role in climate (cryosphere and carbon) and water cycle science.
The NASA NISAR Science Definition Team has developed a set of integrated requirements to respond to the Climate Architecture and other important questions, with ISRO Science participation
Coastal Processes: India
  What is the state of important mangroves?
  How are Indian coastlines changing?
  What is the shallow bathymetry around India?
  What is the variation of winds in India’s coastal waters?

## Slide 4
Interferometric Synthetic Aperture Radar (InSAR) concept
InSAR measures surface deformation by measuring the difference in the phase of the radar wave between the two passes if a point on the ground moves and the spacecraft is in the same position for both passes (zero spatial baseline).

## Slide 5
Instrument Physical Layout
Radar Antenna
Reflector (RAR)
Radar Antenna
Boom (RAB)
I3K Spacecraft Bus
Radar Instrument
Structure (RIS)
Solar Arrays
Radar Antenna
Structure (RAS)
Boom Attach
Point
L-SAR Feed RF
Aperture
(L-FRAP)
L-SAR Digital
Electronics
S-SAR Electronics
(Inside RIS)
L-SAR Radar
Instrument
Controller (RIC)
(Inside RIS)
L-SAR Transmit
Receive Modules (TRM)
S-SAR Feed RF
Aperture
(S-FRAP)

## Slide 6: Reflector / Boom
Reflector (RAR)
  Selected NGAS-Astro Aerospace to provide AstroMesh (AM-1) Perimeter Truss mesh reflector
  Stiff, light-weight design meets pointing and stability requirements
  Completed 20G quasi-static load assessment of the Reflector with the GPS Antenna; no modifications are required to the reflector; launch restraint requires minor modifications
Boom (RAB)
  JPL in-house development joint with the SWOT project
  Completed boom hinge study; selected actuated 4-hinge design
  Currently developing deployment architecture
Boom Deployed
Reflector
Deployed
Reflector/Boom Stowed

## Slide 7: L-SAR Instrument Features
Side looking L-band Synthetic Aperture Radar
Fully polarimetric for classification and Biomass
Repeat pass interferometer for deformation
  Tight Orbit and Pointing Control
  Tight phase stability over imaging time
Split Spectrum for ionosphere mitigation
Multi-beam Array fed Reflector to achieve a 240 km swath
  SweepSAR timing and Digital Beam Forming to reduce ambiguities and preserve resolution / looks
PRF Dithering to fill transmit interference gaps
Seamless mode transitions to minimize data loss
On-board filtering and compression to reduce downlink

## Slide 8
Solid Earth, Ecosystems, Cryosphere Science and Applications Mission
NISAR Uniquely Captures the Earth in Motion
NISAR Characteristic: | Enables:
L-band (24 cm wavelength) | Low temporal decorrelation and foliage penetration
S-band (9 cm wavelength) | Sensitivity to lighter vegetation
SweepSAR technique with Imaging Swath > 240 km | Global data collection
Polarimetry (Single/Dual/Quad) | Surface characterization and biomass estimation
12-day exact repeat | Rapid Sampling
3 – 10 meters mode-dependent SAR resolution | Small-scale observations
Pointing control < 273 arcseconds | Deformation interferometry
Orbit control < 500 meters | Deformation interferometry
L/S-band > 50/10% observation duty cycle | Complete land/ice coverage
Left-only pointing (Left/Right capability) | Uninterrupted time-series Rely on Sentinel-1 for Arctic
Planned Launch: Late 2022
6 AM / 6 PM

## Slide 9: Versatility of SAR for Studying Earth Change
Polarimetric SAR
Use of polarization to determine surface properties
Applications:
  Flood extent (w/ & w/o vegetation)
  Land loss/gain
  Coastal bathymetry
  Biomass
  Vegetation type, status
  Pollution & pollution impact (water, coastal land)
  Water flow in some deltaic islands
Interferometric SAR
Use of phase change to determine surface displacement
Applications:
  Geophysical modeling
  Subsidence due to fluid withdrawal
  Inundation (w/vegetation)
  Change in flood extent
  Water flow through wetlands
9

## Slide 10: Routine Ice Sheet wide velocity mapping
Click to return to main

## Slide 11: Cryosphere – Dynamic Ice Sheets
Jakobshavn Isbrae
Update to Joughin et al., 2014
Requires time-varying horizontal velocities at near-weekly sampling intervals in areas of potential rapid or seasonal change to an accuracy better than 3% plus 10 m/yr (1-sigma) at 500-m resolution (> 80% coverage)
Click to return to main

## Slide 12: Disaster Response
Original ALOS Data © JAXA, METI 2011
Official damage map provided by the New Zealand Government (http://data.govt.nz)
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
2011
185 people killed
> 1000 buildings destroyed
Over US $30 billion damage
M6.3 Christchurch Earthquake
Radar data acquired
by ALOS satellite
Official damage map released
based on ground observations
Damage Proxy Map from radar data
Official damage map updated
based on ground observations
Shakemap released
by USGS NEIC

## Slide 13: Above-ground Dynamics of Forest Biomass
Shimoga
(Karnataka)
N
BIOMASS
Shimoga (KAR.)
2008
BIOMASS
Shimoga (KAR.)
2010
N
YBIOMASS (t/Ha) = A + (B * s0HV) + (C * s0 HH-HV)
s0 is backscattering coefficient in dB and A, B and C are the model coefficients
(RMS Error < 25 t/ha for biomass range within 120 t/ha)
Biomass (ton/ha)
No forest < 20 20 – 50 50 – 80 80 – 120 120 – 160 > 160
model coefficients (A,B & C) have been calculated for different types of forests at several bio-climatic regions
(Deciduous forest dominated by teak (Tectona grandis) vegetation)
ALOS PALSAR-1 HH+HV pol Data

## Slide 14: NISAR Systematic Observations
Persistent updated measurements of Earth
41 Tbits / day total L+S band science data downlink
120 Tbytes / day total L+S band L0-L2 data products
Repeated every 12 day cycle for the life of the mission
J. Doubleday
P. Sharma, JPL
No target conflicts: overlapping targets uses union of all modes specified
Colors indicate different radar modes
14
Hi-res
3-pol
Med-res
2-pol
Notes: Hi-res 3-pol = 40 MHz BW Quasi-quad pol (40 MHz HH/HV + 5 MHz VV/VH
Med-pol 2-pol = 20 MHz BW Dual Pol – 20 MHz HH/HV + 5 MHz HH/HV

## Slide 15: NISAR – Mission Data Products
15

## Slide 16: SWE from InSAR: Theory
Phase shift due to snow:
ΔRns = Path length without snow
θi = Incidence angle
ds = Snow depth
εs = Permittivity
ΔRa = Path length through atmosphere
ΔRr = Path length refracted through snow
θr = Refracted radar angle
(modified from Guneriussen et al., 2001)
ΔSWE (cm) = 2.03 φsnow (radians)
For NISAR parameters
and snow density up to 0.5 g/cm3
θr
ΔRa
ΔRr
ds εs
θi
ΔRns
t0
t1

## Slide 17: Recent L-band InSAR results from SnowEx 2020
UAVSAR pair from Grand Mesa, Feb 13 - Feb 1, 2020
Quantum Spatial Inc (QSI) lidar flights for depth change, Feb 12-Feb 1, 2020
Lidar accuracy ~3-5cm per flight, expected ~6-10cm accuracy for depth/depth change products
UAVSAR depth inversion uses phase change and incidence angle, with measured surface density (200 kg/m^3). No tunable parameters!

## Slide 18
Zoom in on 2km x 2km region with dynamic range in depth
R-value = 0.76, RMSD=4.7cm depth, 0.9cm SWE
Independent high-resolution spatial snow information is critical for evaluation of radar approaches
Recent L-band InSAR results from SnowEx 2020

## Slide 19: Recent L-band InSAR results from SnowEx 2020
Independent field observations of depth change show a mean depth change of 9cm over this period
In these conditions (surface density ~200 kg/m^3), 360 deg phase change can capture 46cm depth change. Reference location and surface density estimate required.
Correlation loss after 3-12 weeks depending on conditions, much shorter in vegetation
SnowEx2021 focused on capturing larger SWE/depth changes, and exploring transition between dry and wet snow
Technique shows promise for defining snow accumulation patterns
More work needed to define limitations in vegetation and steep topography

## Slide 20
CRREL Ground-based L-Band InSAR experiment at Bogus Basin, ID

## Slide 21: Snow melt mapping with SAR
Lund et al., 2020

## Slide 22
Wet snow mapping spring through fall 2015 using Sentinel-1.
Time series of Sentinel-1 SAR data indicating changes in the wet snow cover
Wet snow cover mapping for stream discharge modeling

## Slide 23
Lund J, Forster RR, Rupper SB, Deeb EJ, Marshall HP, Hashmi MZ and Burgess E (2020) Mapping Snowmelt Progression in the Upper Indus Basin With Synthetic Aperture Radar. Front. Earth Sci. 7:318. doi: 10.3389/feart.2019.00318

## Slide 24: Science Users’ Handbook
Describes:
Science and Applications
Mission Science Requirements
Mission Design and CONOPS
Flight System Characteristics
Radar and Measurement Principles
Data Products
Will be revised prior to launch or as necessary
Other major documents:
Cal/Val Plan
Utilization Plan
Application Workshop Reports
21 science and applications white papers
https://nisar.jpl.nasa.gov/files/nisar/NISAR_Science_Users_Handbook1.pdf

## Slide 25: Questions?