## Slide 1
Real Results with Simulated Data: Synthetic Experiments with Data Assimilation of Snow Depth at Basin Scales to Inform Mission Design
Eric Smyth, Mark S. Raleigh, and Eric E. Small | eric.smyth@colorado.edu
1. Snow water equivalent (SWE) from remotely sensed snow depth (e.g. airborne lidar) relies on modeled snowpack density
The PF improves modeled depth, density, and SWE
Motivation / prior research
References
Acknowledgements
[1] van Leeuwen, P. J. (2009). Particle Filtering in Geophysical Systems. Monthly Weather Review, 137(12), 4089–4114. https://doi.org/10.1175/2009MWR2835.1
[2] Smyth, E. J., Raleigh, M. S., & Small, E. E. (2019). Particle Filter Data Assimilation of Monthly Snow Depth Observations Improves Estimation of Snow Density and SWE. Water Resources Research, (4), 1296–1311. https://doi.org/10.1029/2018WR023400
This work was supported by the National Aeronautics and Space Administration (NASA) Terrestrial Hydrology Program under Grant No. NNX17AL41G and NASA FINESST Grant No. 80NSSC19K1374. We thank Richard Essery for making FSM2 code available. (https://github.com/RichardEssery/FSM2). NLDAS-2 forcing data were acquired through NASA GES DISC (https://ldas.gsfc.nasa.gov/nldas/NLDAS2forcing.php).
~32 km
~40 km
2. Assimilating snow depth (SD) with the Particle Filter1 (PF) improves both density and SWE at the point scale2
Goal: Improve modeled SWE at basin scales
Challenge #1: Lack of distributed snow data
Solution: Observing System Simulation Experiment (OSSE)
1
2
3
4
5
6
Generate synthetic “truth” snow depth using model A
Resample depth with an observation filter
Calculate open loop (OL) estimates of SWE
Sample to create intermittent observations
Calculate particle filter estimates of SWE
Compare SWE estimates, relative to OL and an acceptable threshold
Challenge #2: Representation of forest canopy effects
Solution: Assimilation of SD significantly reduces sensitivity
OL MAE:
140 mm
PF MAE:
65 mm
250m grid spacing gives:
~21,500 total pixels
75 particles each pixel
Over 1.6 M simulations
East River Basin, CO
April 20, 2019
Alpine3D
FSM2