## Slide 1
TSMM The Terrestrial Snow Mass Mission
Benoit Montpetit on behalf of all the TSMM team at Environment and Climate Change Canada, Canadian Space Agency and Natural Resources Canada
NASA Community Snow Meeting – Aug. 14, 2024 – Boulder, CO, USA

## Slide 2
7 Ways Snow Mass Information From Space
Will Benefit Canadians
HYDROPOWER & CLEAN ENERGY
Information on snow melt is a strategic requirement to support hydropower generation, a vital economic commodity and key pillar to achieving a net zero energy system
STREAMFLOW FORECASTING
Better understanding of snow melt can improve situational awareness and preparedness for flood events due to changing river flow
NUMERICAL WEATHER PREDICTION
Snow mass measurements can reduce errors in medium-range weather forecasts
WATER RESOURCE SECURITY
Management of water from snow melt is important to ensure water availability for human consumption and to maintain healthy aquatic ecosystems
INFRASTRUCTURE
Snow mass observations can be used to improve disaster resilience and protect the build environment through improved flood forecasting and snow load assessments
AGRICULTURAL PLANNING & FOOD SECURITY
Water from snow safeguards food security by providing essential moisture and mitigating drought risks
HABITAT MONITORING
Keystone wildlife populations of economic and social value, such as caribou, are influenced by snow distribution and properties

## Slide 3: Terrestrial Snow Mass Mission
ECCC and the Canadian Space Agency have partnered on the development of the Terrestrial Snow Mass Mission since 2015
TSMM will deliver the first Ku-band radar measurements from space, which will be used to map snow mass (the amount of water stored in solid form by snow) at 500m resolution, across all of Canada, updated weekly
TSMM-derived snow mass will be used at ECCC to inform analysis of freshwater availability in a changing climate and improve streamflow prediction
Many other sectors require snow mass information, including agriculture, hydropower, and municipal water resource management
Climate change is altering freshwater supply across Canada, including seasonal snow cover, and so understanding impacts on water availability is essential for adaptation planning
First and only satellite EO mission to continuously monitor snow nationally and globally … because water availability and security matters to Canadians everywhere

## Slide 4
TSMM Science Team
Chris Derksen: Mission PI
Benoit Montpetit: SWE Retrieval Science Lead
  Julien Meloche
Vincent Vionnet: Land Surface Modelling Science Lead
  Nicolas Leroux
Marco Carrera: Data Assimilation Science Lead
  Courtney Bayer
  Franck Lespinas
Mike Brady: Data and IT Infrastructure Science Lead

## Slide 5
TSMM Support Team
Mission Management Team
  Jean Bergeron (CSA): Mission Manager
  Fauve Strachan (CSA): Project Manager
Mission Policy Support Teams
  ECCC
  CSA
Mid-Stream Support Teams
  ECCC
  NRCan
  CSA
ECCC Senior Management
  Nathalie Morin: DG of ASTD
  Marc D’Iorio: ADM of S&T
  Jean-François Tremblay: DM
ECCC Economic Research Unit

## Slide 6
Technical Concept
‘Pathfinder’ mission with a specific cost cap: advance innovation and prove scientific viability
Single-aperture dual-frequency Ku-band antenna (13.5/17.25 GHz)
500 m nominal resolution across 250 km swath = coverage of Canada every 5-7 days; 50 m mode across 30 km swath
SAR-on duty cycle of ~25%
Mission duration: at least three winter seasons
Characteristic | Mission Design | Comments
Frequencies | Dual-band operation, 13.5 and 17.25 GHz | Maximize SWE retrieval capability and snow microstructure characterisation
Polarizations | VV; VH | Dual-pol mitigates effects of horizontal layering in the snowpack; cross-pol allows detection of high ocean winds
Ground Resolution | 500 x 500 m | Significant improvement over current 25 km SWE products
Number of Looks | >4 | Multi-looking to enhance radiometric quality
Incidence Angle Range | 25° - 55° | SWE retrieval performance likely to be poorer at shallow and steep incidence angles
NESZ – 13.5 GHz | <-26 dB (VV & VH) | Low NESZ ensures sensitivity to SWE (dry snow), and detection of wet snow cover with weak backscatter
NESZ – 17.2 GHz | <-25 dB (VV & VH) | 
Azimuth and Range DTAR | <-20 dB | Typical DTAR to adequately control ambiguities
Radiometric stability | <0.5 dB | Required temporal consistency of observations
Radiometric accuracy | 1 dB | Enables accurate retrieval of SWE

## Slide 7
SAR/SWE Product Generation
SAR products
Science-to-operations mission
  Run on same system as operational system
  Lower priority than operational sensors
All open/free access L1 data
SAR public archive includes:
  SAR pre-processing (calibration/geocoding/reprojection)
  CEOS SAR ARD
  Imagery over snow covered areas
SWE products
Science-to-operations mission
  Run on parallel system identical to operational system
  Lower priority than operational systems
All open/free access data
  Includes SWE algorithm codes
  L2: SWE from L1 swath
  L3: Standardized gridded weekly L2
  L4: Merged L3/models, gap filled, flagged
  Products available over Canada+Transboundary watersheds

## Slide 8
Science Readiness

## Slide 9
Terrestrial Snow Mass Mission Analysis Approach
We are in the process of applying field campaign data and the mission simulator to demonstrate the viability of all five components of this approach
Assimilation with the Canadian Land Data Assimilation System (CaLDAS)
SVS-2/Crocus snow model simulations
to deliver SWE and microstructure first guess
HRDPS meteorological forcing (2.5 km) + precipitation analysis
Snow wet/dry state algorithm and product development (500m)
Snow water equivalent algorithm and product development (500m)

## Slide 10
Soil Vegetation and Snow (SVS) Version 2
Main objective: enhancing snow simulations in land surface model in support of spaceborne snow missions
Vionnet et al. (2024, in prep)

## Slide 11
Soil Vegetation and Snow (SVS) Version 2
Enhanced parametrizations to simulate snowpack properties across large domains
Revised canopy model for the simulation of snowpack properties in sparse forests
Improved albedo parameterization accounting for the spatial variability of light-absorbing particle deposition on snow
New parametrizations dedicated to the simulation of Arctic snow properties (effects of wind and basal vegetation)
Gaillard et al (2024) TC Discussion
Woolley et al( 2024) TC Discussion

## Slide 12
Canadian Land Data Assimilation Scheme (CaLDAS)
Improve the snow ensemble configuration for valuable forecasts
The current CaLDAS ensemble is under-dispersive for SWE and snow depth outputs
Conducting point scale experiments to determine ensemble sensitivity and best assimilation methods to be implemented in CaLDAS (in MuSA; Alonso-González et al., 2022)
Experimenting with modifying perturbation methods & precipitation phase partitioning for improved snow outputs
Notes: GMD - The Multiple Snow Data Assimilation System (MuSA v1.0) (copernicus.org)

## Slide 13
Data assimilation with MuSA/SVS2
Experimenting with assimilating different observations into SVS2 at point scale
Incorporating SVS2 into the Multiple Snow Data Assimilation System (MuSA)
Extracting observations from the synthetic truths
Comparing the assimilation of different variables
Synthetic experiments at 3 locations spanning different climates
Assimilation using the particle filter method
Assimilation of backscatters at 13 GHz, 17 GHz, and SWE
Impact on bulk SWE and snow vertical properties
Vertical density profiles:

## Slide 14
Forward Modeling of Ku-Band Signal
Optimize/Validate forward modeling approach used in SWE retrieval
Validated forward modeling of Low Ku-Band signal in Arctic
Reduce land surface model layering to “Radar Equivalent Snow” layers improving computation without modifying snowpack geophysical properties
Implementing new radiative transfer equation solver to improve computation and better discriminate scattering mechanisms
Meloche et al (In prep.) TC Discussion
RMSE = 2.6 dB
RMSE = 0.9 dB
RMSE = 1.3 dB
Montpetit et al (2024) TC Discussion
See Julien’s Poster later!
GitHub Snow Microwave Radiative Transfer Model (SMRT) Picard et al.

## Slide 15
Markov Chain Monte Carlo (MCMC):
  Open-Source python library (PyMC)
  Optimizes SSA, Density, Thickness for each layer (3 x N-layer parameters total)
Computation:
  ECCC HPC Linux Server
  Takes ~30 min to run algorithm for 2 snow layers (6 parameters total)
  Could improve to ~30 sec when code is compiled (JAX)
    Need to Jaxify SMRT (again see Julien’s poster!)
SWE Retrieval Algorithm
MCMC

## Slide 16
Uses SVS-2 outputs as inputs
Generates scene using SMRT
Generates L1 product using Phase 0 orbital information
TSMM Data Simulator
Simulated TSMM radar image (VV)
Ottawa River watershed
3 February 2023

## Slide 17
Pre-formulation phase:
  All hands-on deck
  Doubled human resources in last year
Data simulator delivered and working
  Getting ready to produce synthetic experiments
Working on SMRT
Mid-Stream working group
Ongoing Stakeholder Engagement
Science and Applications Plan Drafted
TSMM team fully open to science and programmatic partnerships
  Develop global SWE products
Mission Status
Benoit Montpetit, Ph.D. Research Scientist Climate Research Division benoit.montpetit@ec.gc.ca

## Slide 18: Merci!
Thank you