## Slide 1: A Mission Concept for Measuring Mountain Snow Using P-band Signals of Opportunity: SnoWatch
Steve Margulis, Jessica Lundquist, Simon Yueh, Elias Deeb, Jeff Dozier, Kelly Elder, Dara Entekhabi, Manuela Girotto, Ethan Gutmann, Adrian Harpold, Mimi Hughes, Dennis Lettenmaier, Dongyue Li, Glen Liston, Keith Musselman, McKenzie Skiles, Rashmi Shah, Xiaolan Xu
NASA Community Snow Meeting (Boulder, CO)
14-15 August 2024

## Slide 2
Need for mountain SWE measurements
SnoWatch_002
Snow areas upstream of high water needs
High human water use areas
Snow areas not upstream of high water needs
Lake Mead holds ~35 km3 of mostly snow-derived water, sustaining over 20 million people and over 5 million acres of farmland
Reputable estimates of average water stored in Western U.S. mountain snow show large uncertainty in peak SWE volume
[Fang et al., 2023]
Reputable estimates of average water stored in High Mountain Asia span an even wider range than WUS and highlight the large uncertainty in timing and rate of spring melt
[Liu et al., 2022]
~5x Lake Mead
~1x Lake Mead

## Slide 3: SnoWatch Science Goal and Objectives
Goal: To understand why, when and where mountain snow accumulates and melts, and how these rates and spatial patterns contribute to the water cycle from headwater catch­ments to continental-scale river basins. | 
Science Objective 1 (SO1): | Determine how snowpack accumula­tion processes depend on terrain and synoptic meteorology.
Science Objective 2 (SO2): | Determine how snowmelt rates depend on snow albedo, elevation, peak SWE, synoptic meteorology, forest cover, and snowmelt timing.
Science Objective 3 (SO3): | Determine how warm-season water availability depends on pre-snow soil moisture, peak SWE, and snowmelt, as a function of elevation, terrain, and vegetation cover.

## Slide 4: SnoWatch Observables

## Slide 5
Microwave wavelengths useful for SWE retrievals
Adapted from: https://www.rfpage.com/microwave-frequency-bands/
Ka-band
K-band
Ku-band
X-band
C-band
S-band
L-band
UHF-band
VHF-band
P-band
FM Radio, TV
TV, Radio astronomy, Mobile phones, Military comm.
Telemetry, GPS/GNSS, Air traffic control radar
Weather radar, surface radar, 5G networks
Long-distance radio telecom.,
Wi-Fi
Satellite comm., Radar
Satellite comm., Radar
Radar, Astronomical obs.
Satellite comm.,
Snow-relevant active microwave missions or mission concepts
SnoWatch NASA ESE concept
(P-band)
NISAR, ROSE-L
(L-band)
Sentinel-1
(C-band)
SnowGlobe NASA ESE concept
(Ku-/X-band)
TSMM (CSA) concept,
(Ku-band)
Snow causes volume scattering of incident waves
Snow changes cause phase shift in incident waves

## Slide 6
Why P-band?: Benefits of longer wavelengths

## Slide 7
Why P-band?: A Signal of Opportunity (SoOp)
MUOS (U.S. Military) Signal of Opportunity
  Four geosynchronous communication satellites: allows global coverage up to +/- 60 deg. latitude
  P-band (240-400 MHz): designed for all-weather, all-terrain, and penetration through dense foliage
  Stable long-term signal (since 1978)
Provides a existing and “free” transmitter with signal in band that is otherwise difficult to use for earth science due to RFI  passive SoOp receivers with active radar benefits
Image: JOHNS HOPKINS APL

## Slide 8
Signals of Opportunity + LEO receivers can cover global mountains

## Slide 9
Measuring reflected signal: Interferometric SAR (InSAR)
reflected signal on Day m (e.g. snow-on)
reflected signal on Day n (e.g. snow-off)
SnoWatch uses same physical basis for SWE retrieval as backscattering approaches proposed and validated over ~ 2 decades
(e.g., Sentinel-1, NISAR, ROSE-L)
(e.g., SnoWatch)

## Slide 10
A phase delay corresponds to a wavelength-dependent SWE change.
Interferometry: Phase wrapping (and benefits of P-band)
(L-band)
(P-band)
(C-band)
Implications:
Longer wavelengths introduce less phase wrapping ambiguity due to SWE changes (and improved coherence between scenes)
Phase wrapping errors can be mitigated by using successive pairs of measurements (with smaller SWE changes)

## Slide 11
Reflection from wet snow surface
When snow become sufficiently wet the snow layer becomes opaque and the bulk of reflected signal comes from surface
Measurable phase shift () related to changes in height of snow-air interface (snow depth)
Interferometry: Wet snow
wet snow
Soil
Snow
Air

## Slide 12: P-band SWE and snow depth retrieval: proof-of-concept
Multi-year tower-based implementation at Fraser, CO for two sites: open and with trees
Shah et al. (2017, 2018); Xu et al. (2018)
Dry-snow SWE retrieval
Wet-snow SD retrieval
RMSE:1.2-1.6 cm
RMSE: 7.8-8.9 cm
Demonstrates dry-snow SWE and wet-snow SD retrievals in tree-covered and open plots
Airborne campaign over Grand Mesa, CO and Sierra Nevada, CA
Demonstration of bistatic measurements
Correlation (coherence) seen in reflected signal
“off-the-shelf” JPL receiver bandwidth did not allow for demonstrating phase retrieval
bistatic reflection intensity from SoOpSAR flights over Grand Mesa

## Slide 13: SnoWatch Implementation
Dual frequency (~370 MHz & ~260 MHz) SAR receivers
P-band zenith (direct) and nadir (reflected) antennas
Baselines for SAR processing from (1) dual antenna on each spacecraft and from (2) antennas across spacecraft
MUOS transmitters
3 P-band SAR receivers
Earth rotation used to create separate ground tracks
3 receivers on one orbit plane
zenith antenna
nadir antenna
Baseline design: 3-satellite receiver constellation:

## Slide 14: SnoWatch Implementation
MUOS transmitters
A single receiver provides only one unambiguous reflection point (specular point)
A constellation of receivers reduces the ambiguity of reflected signal to build up a swath via SAR post-processing (SoOp-SAR)
Retrieved phase  SWE
Retrieved amplitude of reflection  Soil moisture
Baseline (3-satellite receivers) characteristics:
Temporal repeat: 6-day
Swath width: ~240 km
Spatial resolution:
along-track: ~40 m;
across-track: ~80 m – 2 km
Sampling pattern contains within-swath and between-swath gaps (more receivers  better resolution and fewer gaps)

## Slide 15: Open Questions/Next Steps
  Primary criticism from ESE review: Need for further validation of retrieval algorithm (how much and what method validation is enough?)
    Ongoing efforts to install tower with P-band receivers in Central Sierra Snow Laboratory; key objective is to get seasonal time series of phase
    Need resources to develop new airborne receivers and undertake new airborne campaigns (future SnowEx efforts?)
  Other criticisms/comments/suggestions:
    Further investigation of dry-to-wet snow transition needed
    Refinement/validation of error budgets involved in phase shift determination
    Stability of MUOS transmitters in future?
  Further test assumptions and choices made in design; Explore synergisms and complementarity with other missions/mission concepts